## Slide 1: SEICHE 2022 Introduction to Arduino Lesson 7– Grounding, ESD, Connecting LEDs
Instructor: Paul Frommeyer
www.paulfrommeyer.com
Corporate Sponsor: DXC Technology

## Slide 2: REMEMBER!
Immediately copy the latest lesson folder (Lesson6 today) from your USB flash drive to your hard drive where you previously copied the other flash drive files (probably Documents folder)

## Slide 3: Lesson Plan Overview
Lesson 1 – Intro and Setup
[may require 2 classes]
• Introduction to class format
• Overview of lesson plan
• Presentation format (monitor, camera, screen, whiteboard)
• Inventory of Arduino kits
• Inventory of USB drives
• Installation of ESP32 serial port drivers (Windows only)
• Installation of Arduino software
• History of Computing
Lesson 2 and 3 – Laptop operation review
• Control panel/Settings location
• Home directories and folder hierarchy
• Arduino file locations
• Search functions
• Open questions and issues
• History of Computing redux
Lesson 4 and 5 – IDE essentials
• The boards manager
• Setting board type
• Installing Libraries
• Loading example sketches
• Finding and selecting the Arduino USB port
• Uploading a sketch to the microcontroller [Example Sketch#1]
• Basic Arduino sketch (program) structure
• Uploading your own sketch [Class Sketch #2]
• History of Telecommunications and Networking – Part 1
Lesson 6 – DC Electricity Basics and DMM Intro
• Quick review: DC vs AC electric currents
• DC current operation
• Voltage vs Amperage (current)
• Ohm’s Law
• Series vs parallel circuits
• Introduction to basic DMM functions and usage
• Measuring voltage [DMM usage #1]
• History of Telecommunications and Networking – Part 2
Lesson 7 – Grounding, ESD, and Connecting LEDs
• Grounding
• The Phantom Menace of ESD
• Resistors!
• LED’s [DMM usage #2, maybe]
• Powering LEDs – Ballast and dropping resistors
• Connecting LEDs to microcontrollers
• Parts of an Arduino Sketch
• ESP32 Specifications – Ampacity
• Let there be Light! – Class Sketch #2
• History of Telecommunications and Networking – Part 3
Lesson 8 – ESP32 External power sources [may require 2 classes]
• Capacitors!
• Microcontroller board power requirements
• Board power input options and grounding
• Components with different voltage requirements – level shifting
• External power circuit design
• Connecting and using transistors
• Pulse width modulation and signal generation
• Connecting and using buzzers – Class Sketch #3
Lesson 9 – Connecting smart LED strips
• Simplified serial communication protocols
• One-wire serial communication protocol
• Hardware vs software serial
• WS2812B and Neopixel connections – Class Sketch #4
• External device power design
Lesson 11 – Connecting LCD and Matrix Displays
• The SPI serial protocol
• SPI connections – Class Sketch #5
• SPI device external power design
Lesson 12 – Connecting sensors [Time permitting]
• Connecting buttons
• Connecting potentiometers and voltage dividers
• Reading buttons and debouncing
• Reading potentiometers
Lesson 13 – Connecting more sensors [Time permitting]
• Connecting I2C sensors and photoresistors
• Using ESP32 integral touch sensors

## Slide 4: Lesson 7 – Connections
Grounding
ESD Safety
Resistors
LEDs
Powering LEDs – Ballast and Dropping Resistors
Connecting LEDs to Microcontrollers
Parts of an Arduino Sketch
WiFi Kit 32 Specifications Review - Ampacity
Let There Be Light – Class Sketch #2
History of Telecommunications and Networking P2 (Time Permitting)

## Slide 5: Grounding – What is a Ground?
https://www.allaboutcircuits.com/technical-articles/an-introduction-to-ground/
In electronics and electrical engineering, it is by convention we define a point in a circuit as a reference point. This reference point is known as ground (or GND) and carries a voltage of 0V. Voltage measurements are relative measurements. That is, a voltage measurement must be compared to another point in the circuit. If it is not, the measurement is meaningless.
The ground reference point is often, but not always—more on this later—represented by a standard (earth) ground symbol.

## Slide 6: Grounding – Earth Ground
https://www.allaboutcircuits.com/technical-articles/an-introduction-to-ground/
Earth ground is exactly as it sounds. It's a ground physically (and electrically) connected to earth via a conductive material such as copper, aluminum, or an aluminum alloy.
A true earth ground, as defined by the National Electrical Code (NEC), consists of a conductive pipe, or rod, physically driven into the earth to a minimum depth of 8 feet.
The earth provides an electrically neutral body, and due to the earth's virtually infinite state of neutrality, it is immune to electrical wavering. It should be noted, however, that "earth being immune to electrical wavering" is, in fact, a generalization. In reality, earth ground is quite the complex subject given all variables and materials that make up the earth. And, earth's electrical potential does indeed experience some isolated areas of varying due to events such as lightning hits, as an example. Power poles, those that are strung throughout neighborhoods, are also connected to ground.

## Slide 7: Electrostatic Discharge – The Phantom Menace
Integrated circuits (ICs) are notorious for being ultra vulnerable to ESD events. Grounded mats (referred to as ESD mats), grounded chairs, and wrist straps provide adequate ESD protection for your ICs by grounding you—thus discharging any static you may have on your body—prior to touching any sensitive components. Most engineers and technicians also wear ESD-safe jackets when working with PCBs and ICs for added protection against possibly damaging components and equipment.
WiFi chips on dev boards are prone to static damage!!!

## Slide 8: Electrostatic Discharge – Protection
Large charges need large grounds, but small charges only need small grounds. Metal the mass of a quarter is sufficient protection for most sensitive electronics, though earth ground is always best. The easiest place to find and attach such metal to a dev board is to just plug it into a breadboard. For particularly sensitive boards (which is us), it may be necessary to “permanently” connect the board ground to one or both of the ground busses on the breadboard. See diagram, above, for how to do this with the WiFi Dev Kit 32
Use the bottom blue rail for grounding, regardless of inside/outside

## Slide 9: Our First Component – Resistors!
Resistors are elements of electrical circuits that resist and reduce the flow of current through the electrical circuit. They can also be used to provide specific voltages to active components. Resistors are available with fixed or variable resistance values. Fixed resistors are ones in which resistance never changes. [Mouser Electronics]
A resistor is a passive two-terminal electrical component that implements electrical resistance as a circuit element. In electronic circuits, resistors are used to reduce current flow, adjust signal levels, to divide voltages, bias active elements, and terminate transmission lines, among other uses. [Wikipedia]
The function of a resistor is measured in Ohms of electrical resistance
Resistors use a color code to indicate resistance and heat dissipation tolerance (wattage)
When electricity passes through a resistor, the voltage of the current drops due to loss of energy. This is called voltage drop, and happens with nearly all components.
Resistors are critical components, ubiquitous in electronic devices

## Slide 10: Light Emitting Diodes
LED – Light Emitting Diode
A semiconductor component similar to a non-emitting diode or transistor
Electrical current through the semiconductor chip produces light
Semiconductor materials used define the color of light produced
The “bluer” the light, the more energy (watts) the LED requires (consumes)
Like all diodes, current can only flow one way through the component, even if its an LED, from + to -
Shorter wavelengths have more energy, so require more energy to create the photons

## Slide 11: Light Emitting Diodes
Anodes (+ terminal) are usually connected to the microcontroller
Cathodes (– terminal) are typically connected to ground
LEDs are constant current devices, drawing between 10 and 20 mA depending on wavelength and emitter size
To prevent burning out the microcontroller, limiting resistors are connected in series with the LED
These “ballast” resistors can be connected to either the anode or cathode of the LED.
It is best practice to connect a single resistor between the microcontroller GPIO pin and the LED anode
There are h4x which ignore this (which we will do!)
Most microcontrollers have internal components for each GPIO pin called pull-up and pull-down resistors that are software controlled. We will study these as part of connecting buttons.

## Slide 12: Ballast and Dropping Resistors
A resistor can be used for current limitation. This resistor is called the ballast resistor. If the supplied voltage is equal to the LED voltage, a resistor will not be needed.
If you are exceeding the LED voltage, you will need a resistor to resist the additional voltage. When calculating the resistor value, you will need to know the voltage drop across the LED first. An example would be a 12V power supply for a 2V LED. With the voltage drop of 2V, you can determine the additional voltage is 10V above the LED value. If the current in the circuit is 200mA, we can now use Ohm’s Law to find the resistor value. With the additional 10V in the circuit and 200mA, the final result will be a 50 ohm resistor. Please note that the power rating for the resistor is important. Power can be calculated as V^2/R, I^2xR, or VxR. In this case, the absolute minimum power rating for this resistor can be 2W, but should be doubled for reliability at 4W.
It’s OK to use a slightly higher value resistor– in fact this is a good idea. Just be mindful of the resistor wattage.
This is one of the most frequent times we use Ohm’s law

## Slide 13: Parts of an Arduino Sketch
All sketches have two parts, or sections, of C++ code
A setup section that runs once when the microcontroller is powered up or reset (note: not when the sketch is first loaded!)
A loop section which runs continuously once the setup section has completed
Technically speaking, these sections are individual functions and are called by a master function which the Arduino IDE elides (hides) from the user
Setup is used to initialize variables, set pin operating modes, and other things to “set the stage” for the main program loop
The loop is where the program steps (statements) for actual processing and events take place

## Slide 14: ESP32 Specifications
All Data From Espressif Systems ESP32 Datasheet
https://www.espressif.com/sites/default/files/documentation/esp32_datasheet_en.pdf
ESP32 Block Diagram
DC Characteristics
Takeaways
Max pin source current: 40mA
Max pin sink current: 28ma
Pull-up resistance: 45KΩ
Pull-down resistance: 45KΩ

## Slide 15: Time to Get Wired
What we are going to do, electrically speaking:
Connect a red LED anode to pin GPIO13 (physical pin 5)
Connect a green LED anode to pin GPIO12 (physical pin 6)
Connect a blue LED anode to pin GPIO14 (physical pin 7)
Connect all LED cathodes to a rail
Connect that rail to the ground pin of the board using a 300 ohm resistor; this places the resistor in series between all three LED cathodes and the power sink (power ground)
300Ω resistor connects here
GPIO13
GPIO12
GPIO14
The asterisk on these GPIO pins means they are INPUT ONLY and cannot be used to send electricity to anything. They can sink (accept) 28mA of current, which is dangerously small for accepting current from LED cathodes

## Slide 16: Connect The Dots
From your Arduino kits:
Select a red, a green, and a blue LED
Select three male-male DuPont jumpers, red, green, and blue
Select a single 330 ohm (probably “R” on the label band) resistor
And get your breadboard out if it’s not already
Then, wire your breadboard up to look like this:

## Slide 17: Let There Be Light
Find the Arduino sketch in your Lesson 7 folder (which you copied from your USB drives, right?) named “ClassSketch2-BlinkDeluxe” and open it in the Arduino IDE
Connect your board to your laptop using USB cable
Remember to set your board type and port speed
Upload the sketch! 
Did it work? You’ve the luck of me Irish ancestors! ♚🍀
It didn’t work? Now you can prove yourself worthy of your maker name and troubleshoot the problem! 🔧😎
What happens if you make the delay values bigger? Smaller? Can you adjust the sketch to perform a “chaser” display?

## Slide 18: History of Telecommunications Part 2
Local Area Networks (LANs)
Wide Area Networks (WANs)
Wireless LAN (WiFi)
Cellular Voice Networks
Cellular data networks
The Internet - Overview

## Slide 19: Local Area Networks
A local area network (LAN) is a group of computers and peripheral devices that share a common communications line or wireless link to a server within a distinct geographic area. A local area network may serve as few as two or three users in a home office or thousands of users in a corporation's central office. Source: TechTarget
Regardless of size, a LAN's single defining characteristic is that it connects devices that are in a single, limited area. Source: Cisco Systems
TL;DR a LAN is a group of computers in a single physical location connected together with physical cabling to allow exchange of data

## Slide 20: Wireless LAN (WiFi)
WLAN/Wi-Fi is a family of wireless network protocols, based on the IEEE 802.11 family of standards, which are commonly used for local area networking of devices and Internet access, allowing nearby digital devices to exchange data by radio waves. These are the most widely used computer networks in the world, used globally in home and small office networks to link desktop and laptop computers, tablet computers, smartphones, smart TVs, printers, and smart speakers together and to a wireless router to connect them to the Internet, and in wireless access points in public places like coffee shops, hotels, libraries and airports to provide the public Internet access for mobile devices. Source: Wikipedia
WLAN is the wireless technology used to connect computers, tablets, smartphones and other devices to the internet. Wi-Fi is the radio signal sent from a wireless router to a nearby device, which translates the signal into data you can see and use. Source: Verizon

## Slide 21: Cellular Voice Networks
A cellular network or mobile network is a communication network where the link to and from end nodes is wireless. The network is distributed over land areas called "cells", each served by at least one fixed-location transceiver (typically three cell sites or base transceiver stations). These base stations provide the cell with the network coverage which can be used for transmission of voice, data, and other types of content. A cell typically uses a different set of frequencies from neighboring cells, to avoid interference and provide guaranteed service quality within each cell. When joined together, these cells provide radio coverage over a wide geographic area. Source: Wikipedia
Cellular networks can be designed to carry voice, data, or both. The earliest cellular networks were voice networks, connecting back to the PSTN (Public Switched Telephone Network).

## Slide 22: Cellular Data Networks
Cellular Network Data is a data connection from the cellular device to the cell site. LTE (4G), 3G and 1X are types of cellular network data connections. Data sessions include, but are not limited to, browsing the Internet such as Google, streaming music, videos and movies, sending and receiving emails, sending and receiving MMS messages, hotspot hosting and application use. While connected to the cellular data network, data usage will pull from the current data plan.
As with all communications between two computers, “data” refers to information encoded into a bitstream of binary numbers. The method used for encoding varies by network layer, device, and communications protocol.

## Slide 23: WiFi and Cellular
WiFi connects to a local router, cellular data connects to a remote router
WiFi has a limited range, cellular data does not

## Slide 24: The Internet - Architecture
The Internet is a “network of networks” used to connect many many LANs and WANs together
Originally the Internet was owned and operated by the US DoD and NSF
Public connectivity became available in 1992 from a company called PSI

## Slide 25: The OSI/ISO Layered Network Model
In a Quora post asking about the purpose of the OSI model, Vikram Kumar answered this way:
“The purpose of the OSI reference model is to guide vendors and developers so the digital communication products and software programs they create will interoperate, and to facilitate clear comparisons among communications tools.”
While some people may argue that the OSI model is obsolete (due to its conceptual nature) and less important than the four layers of the TCP/IP model, Kumar says that “it is difficult to read about networking technology today without seeing references to the OSI model and its layers, because the model’s structure helps to frame discussions of protocols and contrast various technologies.”
If you can understand the OSI model and its layers, you can also then understand which protocols and devices can interoperate with each other when new technologies are developed and explained.
Source: Network World

## Slide 26: ISO/OSI vs The TCP/IP Model
TCP/IP is the data interchange protocol used by the Internet for computer-to-computer (host-to-host) communications
It only loosely follows the formal OSI/ISO reference model
Many consider TCP/IP to be a separate model, but this is not entirely true
We will not be studying TCP/IP in depth, but it is important to know that it exists and is the underlying protocol used in all web comms
Accurate
Inaccurate

## Slide 27: Formal End of Lesson 7
In next week’s exciting episode
Microcontroller board power requirements
Board power input options and grounding
Components with different voltage requirements – level shifting
External power circuit design
Connecting and using transistors
Pulse width modulation and signal generation
Connecting and using buzzers – Class Sketch #3
Don’t forget to return your USB drives!